## Slide 1: Cross-development software laboratory
Juan Zamorano jzamora@datsi.fi.upm.es
Máster Universitario en Ingeniería Informática

## Slide 2: Laboratory assignments
Laboratory
Installation of a native programming environment.
Installation of the cross-platform programming tools.
Real-time On-board data handling (OBDH) program, including temporal analysis
OBDH with Attitude Control System (ACS) and Processor In the Loop (PIL) validation.

## Slide 3: Laboratory kit

## Slide 4: Computer board
USB ST-LINK mini-B connector
GND pin
USB OTG micro-AB connector
PB6 & PB7 pins

## Slide 5: 1. Install the native compiler
Laboratory
Windows:
  Download and run
  gnat-2021-20210519-x86_64-windows64-bin.exe
  Run the GPS application
  Create a new project and enter the source code for hello.adb
  Build and run the executable
MacOS and Linux
  See laboratory guide

## Slide 6: Sample screenshot

## Slide 7: 2a. Install cross compiler for STM32F4
Laboratory
Windows:
  Download and execute the cross-compiler
  gnat-2021-20210519-arm-elf-windows64-bin.exe
  Download and execute the ST-LINK driver
    follow the instructions in readme.txt
  Start the GPS application
  Create a new project
    File > New Project > STM324F compatible > LED demo project template
    Set Project > Properties > Embedded > Connection tool to st-util
  Build and run the executable
  Connect the board to the host computer and flash the executable to the board

## Slide 8: Cross-compilation tools

## Slide 9: Sample screenshot

## Slide 10: 2b. Install the Ada Drivers Library and assignment sources
Laboratory
Ada Drivers Library:
  Download zip file from
  https://github.com/AdaCore/Ada_Drivers_Library
  Unzip the archive and move the resulting folder to your laboratory folder
  Rename the folder to Ada_Drivers_Library
  Open project
    …/Ada_Drivers_Library/examples/STMF4_DISCO/blinky_f4disco.gpr.
  Build the executable and flash it to the board
Assignment sources:
  Download zip file from moodle or
  https://github.com/STR-UPM/OBDH_LABS
  Unzip the archive and move the resulting folder to your laboratory folder

## Slide 11: 3. Real-time OBDH software architecture
Laboratory
period
task
device
data access
AADL : Architecture Analysis & Design Language
AADL components implemented as Ada packages
main procedure: OBDH
additional packages for data definitions & others as necessary

## Slide 12: OBDH tasking system
Laboratory
Two concurrent tasks:
  Housekeeping
    read a sensor (OBC_T)
    use the Ada Drivers Library (ADL) to read the sensor
      STM32.Device
      STM32.ADC
  TTC
    display the sensor value
    Use a serial interface connected to the host PC
      simulate a radio link between flight and ground systems
A protected object for inter-task communication
  Storage
    the housekeeping task puts the sensor value in the storage
    the TTC task gets the value from the storage

## Slide 13: Hardware
Connector pin | Board pin
1 (black) | GND
4 (orange) | PB7
5 (yellow) | PB6

## Slide 14: Host terminal
Laboratory
(Windows — for other platforms see manual)
  Download and install https://www.putty.org
  Find the COM port in device manager (e.g. COM4)
  Open PutTTY and configure as serial connection,115200 bps, 8N1

## Slide 15: Real-time requirements
Task | Period | Deadline | Priority
Housekeeping | 1,0 | 1,0 | 20
TTC | 10,0 | 2,0 | 10
Storage Buffer | — | — | 20
package Housekeeping is
Period : Time_Span := Milliseconds (1000); -- 1s
HK_Priority : constant System.Priority := 20;
...
private
Start_Delay : Time_Span := Milliseconds (1000); -- 1s
task Housekeeping_Task
with Priority => HK_Priority;
end Housekeeping;

## Slide 16: Implementation
task body Housekeeping_Task is
Data : State;
Next_Time : Time := Clock + Start_Delay;
begin
loop
delay until Next_Time;
...
Next_Time := Next_Time + Period;
end loop;
end Housekeeping_Task;

## Slide 17: Timestamps
package Housekeeping_Data is
...
type Mission_Time is new Uint64;
-- Seconds since system startup
type State is
record
Data : Analog_Data;
Timestamp : Mission_Time;
end record;
end Housekeeping_Data;

## Slide 18: Housekeeping
procedure Get (S : out State) is
OBC_T : Analog_Data;
SC : Seconds_Count;
TS : Time_Span;
begin
Sensor.Get (OBC_T);
Split (Clock, SC, TS);
S.Data := OBC_T;
S.Timestamp := Mission_Time (SC);
end Get;

## Slide 19: Storage
package Storage is
procedure Put (Data : State);
procedure Get (Data : out State);
...
-- Real-time attributes
ST_Priority : constant System.Priority := 20;
private
protected Buffer
with Priority => ST_Priority
is ...
...
end Storage;

## Slide 20: Laboratory work
  Open project .../LAB6/RT_housekeeping/real_time_housekeeping.gpr
  Build the executable and flash to board
  Make sure the TTY cable is connected
  Telemetry messages appear on the ground terminal

## Slide 21: Real-time analysis
Laboratory
Task structure
Real-time attributes
Task | T | C | B | D | R | P | CPut | CGet
HK | 1,0 |  |  | 1,0 |  | 20 |  | 
TTC | 10,0 |  |  | 2,0 |  | 10 |  | 
 |  |  |  |  |  | CP | 20 | 20
Housekeeping
1 s
TTC
Storage
10 s

## Slide 22: Average-Case Execution Time (ACET) measurement
Laboratory
A simple dynamic measurement technique will be used in the laboratory
Execute task bodies a number of times and measure times with the board real-time clock
  e.g. for HK task
  the estimated ACET in seconds is C/N
T1 := Clock;
for I in 1..N loop
Get(Data);
Storage.Put (Data);
T := T + Period;
end loop;
T2 := Clock;
C := T2 - T1;

## Slide 23: Laboratory work
  Open project .../LAB6/RT_housekeeping/wcet_meter.gpr
  Study the source code
  Build the executable and flash to board
  Make sure the TTY cable is connected
  Analysis results appear on the ground terminal

## Slide 24: Real-time analysis with measured values
Laboratory
Task | T | C | B | D | R | P | CPut | CGet
HK | 1,0 | 13·10-6 | 4·10-6 | 1,0 |  | 20 | 3·10-6 | —
TTC | 10,0 | 26·10-6 | — | 2,0 |  | 10 | — | 4·10-6
 |  |  |  |  |  | CP | 20 | 20
Task | T | C | B | D | R | P | CPut | CGet
HK | 1,0 | 13·10-6 | 4·10-6 | 1,0 | 17·10-6 | 20 | 3·10-6 | —
TTC | 10,0 | 26·10-6 | — | 2,0 | 39·10-6 | 10 | — | 4·10-6
 |  |  |  |  |  | CP | 20 | 20
All deadlines are guaranteed

## Slide 25: Laboratory work
  Open project .../LAB6/RT_housekeeping/wcet_meter.gpr
  Study the source code
  Build the executable and flash to board
  Make sure the TTY cable is connected
  Analysis results appear on the ground terminal

## Slide 26: Additional tasks
Laboratory
Include the conversion to Celsius in the Display.Put procedure.
  Temperature function of HK_data-converter that can be found in utilities directory can be used.
  OBC_T : MCU internal temperature sensor
    connected to ADC1_IN16 input
    range -40 .. +125 ºC
    14-bit reading VSENSE: 0 .. 4095
    Temperature (in °C) = {(VSENSE – V25) / Avg_Slope} + 25
Symbol | Parameter | Min | Typ | Max | Unit
TL(1) | VSENSE linearity with temperature | - | ±1 | ±2 | °C
Avg_Slope(1) | Average slope | - | 2.5 |  | mV/°C
V25(1) | Voltage at 25 °C | - | 0.76 |  | V
tSTART(2) | Startup time | - | 6 | 10 | μs
TS_temp(2) | ADC sampling time when reading the temperature (1 °C accuracy) | 10 | - | - | μs

## Slide 27: 4. OBDH with ACS software architecture
period
tasks
protected object
Serial
ACS
Host terminal
period
2 s

## Slide 28: OBDH with ACS tasking system
Laboratory
Include three tasks:
  Housekeeping
    read a sensor (OBC_T)
  TTC
    display the sensor value using semi-hosting
  ACS
    control the attitude of the satellite
Host computer runs Simulink model of the environment
  Host and target interchange sensor readings and actuator outputs by serial line

## Slide 29: UPMSat-2
Experimental micro-satellite
  0.50 × 0.50 × 0.60 m, 50 kg
  sun-synchronous orbit
    700 km, 98 min period
  powered by solar panels
  VHF radio dual link 400 MHz
Dipole antenna on top face
  must be visible from Earth at all times

## Slide 30: Attitude control frames
Body reference frame XYZ
  antenna on Z axis
Orbital reference frame X0Y0Z0
  inertial for short intervals
Attitude reference
  align Z with Z0
  slow rotation around Z

## Slide 31: Magnetic attitude control

## Slide 32: Magnetometers / magnetorquers
Laboratory
Magnetometers provide a measurement of the Earth's magnetic field components in the body frame
    b : magnetic field vector
Magnetorquers generate a control torque normal to the orbit
    m: magnetic moment vector
      proportional to the current in each magnetorquer coil
        mi = AN·Ii

## Slide 33: Validation steps: Model-in-the-loop
Preliminary validation of control algorithm
Use a model of the ACS, together with models of the space environment and the spacecraft dynamics, to assess the validity of the control law and the design parameters.
Usually carried out by a control engineer using a simulation tool.
  Simulink is commonly used for ACS development.
Notes: PIL TRL 4

## Slide 34: ACS MIL (Model In the Loop) validation
Laboratory

## Slide 35: Angular velocity stabilization

## Slide 36: Simulink model
Run matlab and open ACS.slx from directory LAB7/ACS.

## Slide 37: Simulink model
Navigate to nominal attitude control.
Simulate and verify angular velocity stabilization

## Slide 38: Validation steps: Processor-in-the-loop
A further step to full validation is running the control software on actual hardware, while still using simulation models of the sensors, actuators, and spacecraft dynamics.
A software validation facility (SVF) uses an auxiliary computer, linked to the OBC by a serial line, to run a simulation model of the Earth's magnetic field and the satellite dynamics.
  In this way, engineering values (Nm and T) can be interchanged.
The code of the control algorithm is generated with the Simulink Code Generator, and compiled and linked with the on-board software using the GNAT development environment.
Functional & real-time behaviour can be validated.
Notes: PIL TRL 4

## Slide 39: Simulink model for code generation
Open control.slx from directory LAB7/ACS_PIL
Select APPS and then Embedded Coder

## Slide 40: Code generation
Take a look to Code generation settings (Settings button)
Generate code with Embedded Coder toolbox (Build button)
Take a look to code generation report (it will pop-up)

## Slide 41: Code generation
The generated C code is located at LAB7/ACS_PIL/control_ert_rtw
Launch gnatstudio and open LAB7/ACS_housekeeping.gpr

## Slide 42: ACS implementation

## Slide 43: ACS Hardware interface

## Slide 44: Study the code
Laboratory
Connect the serial line to the host PC
  as in LAB5 but do not run PutTTY
  serial line will be used for interchanging sensor readings and actuations
Build the executable and debug on the board
  select Build > Bareboard > Debug on board on the top menu
Type continue or just c on the debugger console
  The program starts
The Red LED does not blink because ACS is waiting sensor inputs from SVF.

## Slide 45: Simulink model por PIL validation
Open ACS_PIL.slx from LAB7/ACS_PIL directory
Navigate to nominal attitude control.

## Slide 46: Study the model
Laboratory
The control block has been replaced by a connection to the serial line
  edit the serial configuration block and put the name of the serial line of your PC
  additional rate transition blocks have been added to ensure a proper communication
A Real-Time pacer has been added to the model to set the simulation speed
  Speedup = 1 should be used but it is too slow
Start the simulation and verify angular velocity stabilization
  Now ACS runs and red LED is toggled

## Slide 47: Simulink PIL validation
Compare angular velocity stabilization with the original full-Simulink model.

## Slide 48: Make changes and play
Laboratory
Default parameters for control blocks can be changed in Ada source file ACS-parameters.ads
  Default_omega is the consigned angular velocity
  Default_MT_Working contains the operational magneto-torques
  In UPMSat-2 the parameters can be changed by TC
The initial angular velocity can be changed in Simulink source code initialization.m
  omega_BI_B0 = [0.1;-0.1;-0.1];

## Slide 49: Validation steps: Hardware-in-the-loop
The next step is to include a model of the actual magnetometers and magnetorquers in the simulation model, and connect their inputs and outputs to the OBC hardware by means of its analog and digital input and output lines.
This simple kind of HIL setup allows the operation of input/output devices, as well as signal conditioning hardware and software, to be validated.
Full HIL validation, though, requires using the real magnetometers and magnetorquers hardware and, ultimately, the whole satellite structure, on a setup which enables the attitude of the spacecraft to evolve in a free fashion.
Notes: PIL TRL 4

## Slide 50: Technology Readiness Level (TRL)
The technical maturity of instruments and spacecraft sub-systems with respect to a specific space application are classified according to a "Technology Readiness Level" (TRL) on a scale of 1 to 9. ESA uses the ISO standard 16290 Space systems – Definition of the Technology Readiness Levels (TRLs) and their criteria assessment.
ISO Technology Readiness Level Summary
TRL Level Description
1 Basic principles observed and reported
2 Technology concept and/or application formulated
3 Analytical and experimental critical function and/or characteristic proof-of-concept
4 Component and/or breadboard functional verification in laboratory environment
5 Component and/or breadboard critical function verification in relevant environment
6 Model demonstrating the critical functions of the element in a relevant environment
7 Model demonstrating the element performance for the operational environment
8 Actual system completed and accepted for flight ("flight qualified")
9 Actual system "flight proven" through successful mission operations
http://sci.esa.int/sci-ft/50124-technology-readiness-level

## Slide 51: Hardware In the Loop
Laboratory
To reach a higher TRL, a more realistic operational environment is needed
  In UPMSat-2, ADC hardware was also included in the loop
  A SVF host with analog input/outputs had to be set up in order to generate magnetometer outputs and read magnetorquer actuations.
Much more sophisticated operational environments are possible.
  However, they have a high cost

## Slide 52: Hardware In the Loop
Laboratory
To reach a higher TRL, a more realistic operational environment is needed
  In UPMSat-2, ADC hardware was also included in the loop
  A SVF host with analog input/outputs had to be set up in order to generate magnetometer outputs and read magnetorquer actuations.
Much more sophisticated operational environments are possible.
  However, they have a high cost

## Slide 53: Student assignment
Laboratory
Students have to write a brief report of about 2-3 pages about the work done including an analysis about cross-development environment for embedded systems and the main differences with a native environment.
The schedulabilty analysis for LAB6 must be included.
The report can contain recommendations to improve the assignment and personal opinions.
If you have made the proposed changes or any other, you should write them in the report and upload the code too.
Moodle is the selected platform for uploading assignment and the deadline is December 10th.